## Slide 1: VMware NSX 6.1
What’s New

## Slide 2: Topics
  Overview
  Equal Cost Multipath
  DHCP Relay
  L2VPN Enhancements
  Distributed Firewall Enhancements
  Load Balancing and ADCaaS Enhancements
  Platform Enhancements
  vCloud Automation Center 6.1 Integration
  Resources

## Slide 3: Overview

## Slide 4: What’s New: Data Plane
Consumption
Services
Data Plane
Operations
NSX Edge
Active-Active with Scale-Out (ECMP)

## Slide 5: What’s New: Services
Consumption
Services
Data Plane
Operations
Distributed Firewall Improvements
Firewall Ecosystem Enablement
Multi-Site & Hybrid Cloud Enablement
Layer 2 VPN , Active-Active DC, SRM Validation
LBaaS
UDP support, ecosystem enablement
DDI DHCP Relay

## Slide 6: What’s New: Operations
Consumption
Services
Data Plane
Operations
Operations Guides & Best Practices
Integration with Existing Tools
Riverbed, Gigamon, NetScout, EMC Smarts
Analytics
VMware vCenter Ops, Log Insight
Firewall Operations
Tufin, Algosec
New NSX Partners & Service Categories
Physical-to-Virtual Services
Operations & Visibility
Application Delivery Services
Security Services

## Slide 7: What’s New: Consumption
Consumption
Services
Data Plane
Operations
vCloud Automation Center
More topologies and on demand use cases

## Slide 8: Equal Cost Multipath (ECMP)

## Slide 9: Equal Cost Multipath
  New in 6.1
  Active/Active HA model with up to eight (8) NSX Edges
  Increased bandwidth for North-to-South communication
  Speed up recovery in an NSX Edge failure scenario
  ECMP is disabled on the Distributed Logical Router, by default
  ECMP on the Distributed Logical Router is new to 6.1 SW NSX Releases

## Slide 10: Logical Routing High Availability
External Network
DLR Control VM
ECMP HA Model
Active/Standby HA Model
Standalone HA Model
Active
Standby
Active/Standby HA Model
Web1
App1
DB1
NSX Edge
Distributed Routing
Notes: Active/Standby is the traditional model
Standalone is two-active model
ECMP HA is the many active model
(Standalone HA and ECMP HA are both ECMP enabled models)

## Slide 11: Standalone HA Model: 2 NSX Edges (1)
  North-to-South traffic is handled by one of two active NSX Edges
  Recommendations
    Aggressively tune the hello/holdtime routing timers (1/3 seconds)
    No need for deploying standby unit for any active NSX Edge
    vSphere HA should be enabled for the NSX Edge virtual machines
  Stateless behavior in Active/Active model
    No support for stateful FW, LB, NAT across the active NSX Edges
DLR
Physical Router
VXLAN
VLAN
Core
Active
Routing
Adjacency
Routing
Adjacency
E2
E1
Web
DB
App

## Slide 12: Standalone HA Model: 2 NSX Edges (2)
DLR
Physical Router
VXLAN
VLAN
Core
Failed
Active
E2
E1
X
Web
DB
App
  On failure of NSX Edge E1:
    The DLR times-out the routing adjacency with the failed Edge
    Routing tables are updated to reference the second active unit
Routing
Adjacency
Routing
Adjacency

## Slide 13: ECMP HA Model: Up to 8 NSX Edges (1)
DLR
E3
E1
Physical Router
E2
…
Core
VXLAN
VLAN
Routing
Adjacencies
E8
Web
DB
App
  Up to eight NSX Edges supported
  North-to-South traffic is handled by all active NSX Edges
  ECMP can be enabled and configured on both the DLR and NSX Edge
  Traffic is hashed across paths based on the Src/Dst IP address values
  When ECMP is enabled, the NSX Edge firewall is disabled
  Stateless behavior in Active/Active model
    No support for stateful FW, LB, NAT across the active NSX Edges

## Slide 14: ECMP HA Model: Up to 8 NSX Edges (2)
DLR
E3
E1
Physical Router
E2
…
Core
VXLAN
VLAN
Routing
Adjacencies
E8
Web
DB
App
X
  On failure of an NSX Edge:
    The DLR and physical router time out the routing adjacencies
    Routing table entries are removed
    Corresponding flows are re-hashed thru the remaining active units

## Slide 15: ECMP HA Model: Up to 8 NSX Edges (3)
DLR
E3
E1
Physical Router
E2
…
Core
VXLAN
VLAN
Routing
Adjacencies
E8
Web
DB
App
X
  Recommendations
    Aggressively tune the hello/holdtime routing timers (1/3 seconds)
    No need for deploying standby unit for each active NSX Edge
    vSphere HA should be enabled for the NSX Edge virtual machines

## Slide 16: DHCP Relay

## Slide 17: DHCP (1)
  New in 6.1
  DHCP relay configuration can be applied on the DLR and the NSX Edge
  Supports multiple relay agents along the same data-path
  Many DHCP servers can be configured to receive relayed messages

## Slide 18: DHCP (2)
Relay DHCP messages from virtual machines in the NSX domain to existing external DHCP servers
  Leverage existing DHCP infrastructure
DHCP server Y
Server X
Server Y
Server X
VM
Logical SW
Logical SW
Distributed router
DHCP server X

## Slide 19: CLI (1)
  CLI: show service dhcp
    Enhanced output in 6.1

## Slide 20: CLI (2)
  CLI: show config dhcp
    Enhanced output in 6.1
vShield Edge DHCP Config:
{
"dhcp" : {
"relay" : {
"maxHopCounts" : 10,
"servers" : [
"192.168.1.2"
],
"agents" : [
{
"interface" : "vNic_1",
"giaddr" : [
"192.168.2.1"
]
}
]
},
"logging" : {
"enable" : true,
"logLevel" : "debug"
},
"enable" : true,
"bindings" : {},
"leaseRotateTime" : 900,
"leaseRotateThreshold" : 10000
}
}

## Slide 21: L2VPN Enhancements

## Slide 22: NSX Multi-Site L2VPN Enhancements
  VXLAN and VLAN trunk support
    Multiple internal networks can be extended per edge
    Edge can handle more than 10 networks by allowing multiple networks to be trunked on a single interface
  L2 VPN Client Appliance unbundled from NSX management
    Solution will work without NSX or vCenter Server on the client-side
  Egress Optimization is supported
    L2 ARP filtering of remote gateway
  Ability to route over tunnel to remote networks that aren’t stretched at L2
  Operational improvements: Support for HA and expanded CLI command set
  Extended platform support
    Can be used with earlier vSphere versions and ESXi-only environments
Notes:   VXLAN and VLAN trunk support:
  New 6.1
  L2 VPN Client Appliance unbundled from NSX management:
  New 6.1
  Egress Optimization is supported
    Enhanced in 6.1
  Ability to route over tunnel to remote networks that aren’t stretched at L2
  New 6.1
  Operational improvements: Support for HA and expanded CLI command set
  Enhanced in 6.1
  Extended platform support
    New in 6.1

## Slide 23: NSX Multi-Site L2VPN
SSL secured L2 extension technology over any IP network
Separate NSX Edge GWs run as server & client
Independent of vCenter Server boundaries
Managed and Unmanaged options
UI and API based configuration
Able to bridge any combination of VLAN or VXLAN networks
No specialized hardware required (will leverage AES-NI CPU instruction set where available)
Supports both Enterprise and Hybrid Cloud use cases
Features
Benefits
L2 VPN
Internet / WAN
Enterprise
NSX Edge Services GW L2VPN Client
NSX Edge Services GW L2VPN Server
L2 VPN
Internet / WAN
Public Cloud
Hybrid Cloud
NSX Edge Services GW L2VPN Client
NSX Edge Services GW L2VPN Server

## Slide 24: NSX Multi-Site L2VPN: Enterprise
Datastore 1
Datastore 2
vCenter
Server
Site A
Site B
vCenter
Server
SSL
SSL
L3 Network
L2VPN Client
L2VPN Server
VM1
VM2
VLAN 200 172.16.20.0/24
Tunnel ID 20
VM3
VM4
VLAN 2000 172.16.20.0/24
Tunnel ID 20
VM3
VM4
VLAN 1000 172.16.10.0/24
Tunnel ID 10
Site B NSX Edge GW
Site B
Uplink Network
VLAN Trunk Interface
VM1
VM2
VLAN 100 172.16.10.0/24
Tunnel ID 10
Site A NSX Edge GW
Site A
Uplink Network
VLAN Trunk Interface
Notes: Add connectivity over an L3 network between sites (could be WAN or a network controlled by enterprise)
Site A has it’s own management components (vCenter, NSX Manager and Controllers), and in this example we are extending VLAN 100 and marking it with a tunnel ID of 10, then we also add VLAN 200 tunnel ID 20 and both VLANs are trunked to the NSX Edge GW.
Site B has similar steps where we trunk VLANs 1000 and 2000
Then we eanble L2VPN server at Site B, client on Site A and create an SSL tunnel which bridges networks together that share the same tunnel ID so that they are in the same L2 segment
Network A and Network B can be any type (VXLAN, VLAN), here we are extending VLAN 100 in Site A to 1000 in Site B, and 200 to 2000.
To overcome the above issue, we will change the behavior of step (d) above. Instead of sending ARP request with IP of Edge 1 (11.1) in ARP header, we will send ARP request with IP as 0.0.0.0.
Thus when the ARP request reaches D (as in step (e) above), D does not update it's ARP cache but still responds back with it's ARP reply.
This technique of sending ARP request with 0.0.0.0 as source IP in ARP header is used to detect duplicate address.

## Slide 25: NSX Multi-Site L2VPN: Hybrid Cloud
Site A
Site B
vCenter
Server
SSL
SSL
L3 Network
L2VPN Client
L2VPN Server
VM3
VM4
VXLAN 5001 172.16.20.0/24
Tunnel ID 6
VM1
VM2
VLAN 51 172.16.20.0/24
Tunnel ID 6
VM1
VM2
VLAN 50 172.16.10.0/24
Tunnel ID 5
Site A Standalone Edge
VLAN Trunk Interface
Site A
Uplink Network
ExistingRouter
VM3
VM4
VXLAN 5000 172.16.10.0/24
Tunnel ID 5
Site B NSX Edge GW
Site B
Uplink Network
VXLAN Trunk Interface
Notes: This slide, shows the standalone edge being used in combination with an existing router at site A – so it’s more of a hybrid cloud use case.
Site A does not require management components such as NSX Manager and NSX Controllers. In our example we are extending VLAN 50 with a tunnel ID of 5, then we also add VLAN 51 tunnel ID 6 and again both VLANs are trunked to the standalone NSX Edge GW.
Site B has a managed NSX Edge with a VXLAN trunk for the two networks being extended.
Then we create an SSL tunnel using the L2VPN
Here we are extending VLAN 50 in Site A to VXLAN 5000 in Site B, and 51 to 5001.
Our third solution leverages the L2VPN solution in the NSX Edge Services GW.
This is a deployment model that can fit both enterprise use cases across 2 vCenter Servers, and Service Provider use cases to provide L2 extension between a customers on premise resources and off premise cloud capacity from the SP.
We start with Compute, network and storage resources at both local and remote sites.
Then Add connectivity over an L3 network between sites
Site A has it’s own management components (vCenter, NSX Manager and Controllers), and we either deploy a logical network, or use an existing network then add an NSX Edge GW.
Site B has similar steps either done by the enterprise, provider or self-service
Then we create an SSL tunnel using the L2VPN feature of NSX for vSphere which bridges the two networks together so that they are on the same broadcast domain
Network A and Network B can be any type (VXLAN, VLAN)
L3 Network typically internet (although could be enterprise L3 network)
Also applies to enterprise, who doesn’t need NSX at Site A
Our configuration, has one edge GW configured as an L2VPN client – here we select the internal network (VLAN backed dvPortgroup in the example) we are extending and define the L2 VPN server IP, Port and credentials
The Site B Edge is configured as an L2VPN server, we again select the internal network (VXLAN logical switch in our example), choose the listener IP and Port (which matches what was configured on the client), encryption algorithm and certificate
The Edges at each site are configured with the same internal IP address to enable local egress, and ensure VMs do not need to change network settings after being migrated.
As L2 is performed before routing, we also require some firewall rules to ensure that VMs don’t send traffic to the remote site as their default gateway. This is accomplished by creating Edge Firewall rules that only allow the local subnet to access the gateway address.

## Slide 26: Firewall Enhancements

## Slide 27: Reject Action
New option in rule action field
  Reject action will send back to initiator:
    RST packets for TCP connections
    ICMP unreachable with administratively prohibited code for UDB, ICMP, and other IP connections.
Notes: New in 6.1

## Slide 28: Advanced Rule Filtering
Apply Filter
Remove Filter
Advanced Rule Filtering: filter policy rule display.
Criteria for filtering:
  Source / Destination: IPv4/IPv6 Addresses, Any, VM name
  Action: Any / Allow / Block / Reject
  Enabled: Any / Enabled / Disabled
  Logging: Any / Enabled / Disabled
  …
Notes: New in 6.1

## Slide 29: Combined Firewall UI
Applied to DFW or ESG
Central management of rules applied on the distributed firewall or any NSX Edge Services Gateway (ESG)
Notes: New to 6.1

## Slide 30: Partner Security Services (1)
New tab under Firewall menu to configure traffic redirection policy rule
Source/Destination:
Cluster
DC
DVS port group
IP Sets
Logical Switch
Resource Pool
Security Group
vAPP
VM
vNIC
Notes: New to 6.1

## Slide 31: Partner Security Services (2)
Service:
Same list as service for DFW policy rules
Notes: New to 6.1

## Slide 32: Partner Security Services (3)
Action:
Redirect
Do not redirect
Redirect to:
Any 3rd party vendor
Registered with NSX
Notes: New to 6.1

## Slide 33: Operations Enhancements
Logging:
  Rule messages are now stored in a dedicated file
Threshold Event:
  Configurable threshold values for:
    CPU
    Memory
    CPS (connections per second)
  Syslog and NSX event messages triggered when value exceeds threshold
IP Flow Information Export (IPFIX):
  Enabled in Flow configuration > Configuration > IPFIX
  DFW exports IPFIX information about processed flows
  Supported collectors:
    Plixer Scrutinizer Collector
    Netflow Integrator
Notes: Logging:
  Rule messages are now stored in a dedicated file
  New to 6.1
Threshold Event:
New to 6.1
  Configurable threshold values for:
    CPU
    Memory
    CPS (connections per second)
  Syslog and NSX event messages triggered when value exceeds threshold
IP Flow Information Export (IPFIX):
  New to 6.1

## Slide 34: Load Balancing and ADCaaS

## Slide 35: Load Balancing Enhancements
Protocol additions:
  UDP, FTP
LB method additions:
  HTTP header/URL
Health Check additions:
  UDP
Miscellaneous enhancements:
  L4 stateful failover
  VC container support to add members to pool
  Configurable persistence expire time
Partner integration enhancements:
  LB/ADC partner integrations
    NSX centrally configures all network and security services (LB included)

## Slide 36: NSX / F5 Joint Solution Overview
Any Application
(without modification)
Virtual Networks
VMware NSX Network Virtualization Platform
Logical L2
Any Network Hardware
Any Cloud Management Platform
Logical Firewall
Logical
Load Balancer
Logical L3
Logical
VPN
Any Hypervisor
Logical
Load Balancer
Virtual IP: 172.168.1.1
Member pool: 10.0.0.1, 10.0.0.2
ADC template (iApp):
Web Gold
Features
  NSX integrates with F5 BIG-IQ
  F5 Admin defined iApps published to NSX Manager
  BIG-IPs VEs get automatically deployed, licensed and configured
  User can consume F5 iApps from NSX UI or API
Benefits
  Compatible with all NSX features
  Seamless support for virtual networks and traditional networking with VLANs
  Familiar workflows for all teams (in NSX , and in F5 BIG-IQ)
  Supports virtual form factor of F5 appliances
  Limitations on some F5 features (no multi-tier iApp, no F5 security modules)
  Future support for any CMP including vCAC
  Future support for physical appliances in the further release

## Slide 37: Platform Enhancements

## Slide 38: Controller Security
Password strength requirement similar to NSX Edge 6.0
  12-255 characters in length
  Must contain at least one of each:
    Lowercase character
    Uppercase character
    Number
    Special character
  Cannot contain
    The word admin
    Any character repeated three or more times
Notes: Enhanced in 6.1

## Slide 39: One-Click Controller Upgrades
If an upgrade is available:
  An upgrade link is available in the UI
  A one-click upgrade is provided for the administrator
Notes: New in 6.1

## Slide 40: Host-Level Packet Capture
CLI-based troubleshooting tool
  Can operate at any stage in the packet lifecycle:
    dvPort
    Vmknic
    Uplink
  Extensive range of filters:
    Source/destination MAC
    IP protocol
    VLAN ID
    VXLAN ID
    Ports
    Many others…
  Pcap format output
    Export for use with common protocol analyzers
Notes: Host-level packet capture on an ESXi host is not new – that NSX can now leverage it is a new feature to 6.1.

## Slide 41: Traceflow
Provides a coordinated way of capturing packet exchanges between VTEPs
  The NSX Controller leverages host-level packet capture across two participating hosts
1
2
3
4
5
6
Host A
VTEP1
Host B
VTEP2
ping
Notes: New to 6.1

## Slide 42: vCloud Automation Center 6.1 Integration

## Slide 43: vCloud Automation Center 6.1 Integration (1)
Connectivity:
  Network Profiles for On-Demand Network Creation
    Routed, NAT, private, external profiles based on Application Topology
  NSX Distributed Logical Router (DLR) Support
    Connect to pre-created External networks
    Optimize east-west traffic by connecting On-Demand Logical Switches to a pre-created DLR
  All On-Demand Edges use NSX 6.1 version
Availability:
  On-demand Load Balancer in One-Armed Mode or Inline Mode
    NSX Load Balancing configuration used
Extensibility:
    Business Logic moved to NSX vCO Plugin
Notes: Connectivity:
  Network Profiles for On-Demand Network Creation
    Enhanced and expanded in 6.1
  NSX Distributed Logical Router (DLR) Support
    Enhanced and expanded in 6.1
Availability:
  On-demand Load Balancer in One-Armed Mode or Inline Mode
    Enhanced and expanded in 6.1
Extensibility:
    Business Logic moved to NSX vCO Plugin
Enhanced in 6.1

## Slide 44: vCloud Automation Center 6.1 Integration (2)
Security:
  App Isolation
    Automatic creation of security group per app with default policy to permit traffic between tiers and block all inbound/outbound traffic
  On Demand creation of Security Groups based on Security Policies
    Select pre-defined NSX security policies which apply to security groups for component VMs
    Allows self-service consumption of DFW Rules, AV, DLP, IDS/IPS, Vulnerability Management
  Security Tags
    Select pre-defined NSX security tag which is applied to VMs and used to dynamically place workloads in security groups
Notes: Security:
  App Isolation
    Enhanced in 6.1
  On Demand creation of Security Groups based on Security Policies
    Enhanced in 6.1
  Security Tags
    Enhanced in 6.1

## Slide 45: vCloud Automation Center 6.1 Integration (3)
Product Compatibility Matrix:
  vCO server embedded with vCAC VA includes the NSX vCO plugin by default
  A standalone vCO server is recommended for production
    Requires installation of the NSX plugin
Product | Version
vCAC | 6.1
vCO Server | 5.5.2
NSX vCO Plugin | 1.0
NSX vSphere | 6.1.0

## Slide 46: Resources

## Slide 47: Documentation and Software
Product Documentation: (Live after GA) https://www.vmware.com/support/pubs/nsx_pubs.html
  NSX for vSphere Installation and Upgrade Guide
  NSX for vSphere Administration Guide
  NSX for vSphere API Reference Guide
  NSX for vSphere Command Line Interface Reference
Software available for download by customers (Live after GA)
  NSX-v upgrade bundle
  NSX-v OVA
  vShield upgrade bundle
  Standalone Edge for L2VPN
  VCO Plug-in and README

## Slide 48: Key Points
Questions?